Pin assignments: sorted by

Pin assignments: sorted byPin assignments: sorted bybond pad number

§        Bond pads are numbered from 1 to 100. They are numbered counter-clockwise starting at the upper right corner;

§        The origin of the coordinates (point (0,0)) is the lower left corner;

§        The (X,Y) coordinates are the centre of the bond pads;

§        The ASIC dimensions are 3850 mm´3850 mm (Extra 20 mm per side might have to be added to account for the scribe line. In case of need, I could send you a sample of the ASIC.)

§        To facilitate identifying the critical signals:

o       Ground signals marked green

o       Power signals marked red

o       Fast serial signals marked blue

§        Signals marked blue will require controlled impedance transmission lines:

o       Signal ld_cathode: 25 Wtransmission line (both bond pads 7 and 8 connect to the same line)

o       Signals serial_line_p and serial_line_p: 50 Wcoplanar transmission line (bond pads 13 and 14 connect to one conductor of the coplanar transmission line and the bond pads 15 and 16 to the other)

§        The package should contain a GROUND and a POWER plane.

§        All power signals must be directly connected to the power plane. These signals are VDD, VDDA1, VDDA2, VDDA3 and VDDA4.

§        The two signals called “ld_anode” must be also directly connected to the power plane.

§        At least three ground pins must be made also thermal pins. If possible, these pins should be located under the ASIC area.

| Bond Pad # | X (m) | Y (m) | PIN Number | Name | Type | Description |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | 3438 | 3780 | <![ENDIF]> | GND | pwr | <![ENDIF]> |
| 2 | 3312 | 3780 | <![ENDIF]> | VDDA1 | pwr | serializer power |
| 3 | 3188 | 3780 | <![ENDIF]> | VDDA2 | pwr | laser diode bias power |
| 4 | 3062 | 3780 | <![ENDIF]> | GND | pwr | <![ENDIF]> |
| 5 | 2938 | 3780 | <![ENDIF]> | GND | pwr | <![ENDIF]> |
| 6 | 2812 | 3780 | <![ENDIF]> | VDDA3 | pwr | laser driver power |
| 7 | 2687 | 3780 | <![ENDIF]> | ld_cathode | out | laser driver output |
| 8 | 2562 | 3780 | <![ENDIF]> | ld_cathode | out | laser driver output |
| 9 | 2437 | 3780 | <![ENDIF]> | ld_anode | pwr | laser diode power (or VDDA3) |
| 10 | 2312 | 3780 | <![ENDIF]> | ld_anode | pwr | laser diode power (or VDDA3) |
| 11 | 2188 | 3780 | <![ENDIF]> | VDDA3 | pwr | laser driver power |
| 12 | 2062 | 3780 | <![ENDIF]> | GND | pwr | <![ENDIF]> |
| 13 | 1938 | 3780 | <![ENDIF]> | serial_line_n | out | differential bit-stream output |
| 14 | 1812 | 3780 | <![ENDIF]> | serial_line_n | out | differential bit-stream output |
| 15 | 1688 | 3780 | <![ENDIF]> | serial_line_p | out | differential bit-stream output |
| 16 | 1562 | 3780 | <![ENDIF]> | serial_line_p | out | differential bit-stream output |
| 17 | 1437 | 3780 | <![ENDIF]> | GND | pwr | <![ENDIF]> |
| 18 | 1312 | 3780 | <![ENDIF]> | VDDA3 | pwr | laser driver power |
| 19 | 1187 | 3780 | <![ENDIF]> | VDDA1 | pwr | serializer power |
| 20 | 1062 | 3780 | <![ENDIF]> | GND | pwr | <![ENDIF]> |
| 21 | 912 | 3780 | <![ENDIF]> | i2c_addr<1> | in | I2C device address (pull-down) |
| 22 | 788 | 3780 | <![ENDIF]> | i2c_addr<2> | in | I2C device address (pull-down) |
| 23 | 662 | 3780 | <![ENDIF]> | i2c_addr<3> | in | I2C device address (pull-down) |
| 24 | 538 | 3780 | <![ENDIF]> | i2c_addr<4> | in | I2C device address (pull-down) |
| 25 | 412 | 3780 | <![ENDIF]> | conf_i_pll | in | selects PLL bias current (pull-down) |
| 26 | 69 | 3438 | <![ENDIF]> | i2c_addr<5> | in | I2C device address (pull-down) |
| 27 | 69 | 3287 | <![ENDIF]> | GND | pwr | <![ENDIF]> |
| 28 | 69 | 3162 | <![ENDIF]> | i2c_addr<6> | in | I2C device address (pull-down) |
| 29 | 69 | 3037 | <![ENDIF]> | conf_glink | in | “1”: G-Link (pull-up) “0”: 8B/10 |
| 30 | 69 | 2913 | <![ENDIF]> | VDDA4 | pwr | PLL power |
| 31 | 69 | 2787 | <![ENDIF]> | GND | pwr | <![ENDIF]> |
| 32 | 69 | 2662 | <![ENDIF]> | conf_laser | in | “1”: laser-driver (pull-up) “0”: line-driver |
| 33 | 69 | 2538 | <![ENDIF]> | conf_wmode16 | in | “1”: 16-bit (0.8 Gbit/s) “0”: 32-bit (1.6 Gbit/s) |
| 34 | 69 | 2412 | <![ENDIF]> | reset_b | in | master reset |
| 35 | 69 | 2287 | <![ENDIF]> | test_shift | in | enables test of internal logic (pull-down) |
| 36 | 69 | 2163 | <![ENDIF]> | GND | pwr | <![ENDIF]> |
| 37 | 69 | 2037 | <![ENDIF]> | VDD | pwr | <![ENDIF]> |
| 38 | 69 | 1912 | <![ENDIF]> | JTAGTCK | in | JTAG clk (pull-high) |
| 39 | 69 | 1787 | <![ENDIF]> | dav | in | data available |
| 40 | 69 | 1662 | <![ENDIF]> | JTAGTMS | in | JTAG mode select (pull-high) |
| 41 | 69 | 1534 | <![ENDIF]> | cav | in | control data available |
| 42 | 69 | 1412 | <![ENDIF]> | JTAGTDO | out | JTAG data out |
| 43 | 69 | 1287 | <![ENDIF]> | conf_i_ld<0> | in | selects laser driver bias current (pull-down) |
| 44 | 69 | 1162 | <![ENDIF]> | JTAGTDI | in | JTAG data in (pull-up) |
| 45 | 69 | 1037 | <![ENDIF]> | conf_i_ld<1> | in | selects laser driver bias current (pull-down) |
| 46 | 69 | 912 | <![ENDIF]> | JTAGTRST_b | in | JTAG reset (pull-down) |
| 47 | 69 | 788 | <![ENDIF]> | GND | pwr | <![ENDIF]> |
| 48 | 69 | 662 | <![ENDIF]> | VDD | pwr | <![ENDIF]> |
| 49 | 69 | 538 | <![ENDIF]> | test_analog | out | test output |
| 50 | 69 | 412 | <![ENDIF]> | ready | out | transmitter ready |
| 51 | 412 | 69 | <![ENDIF]> | SCL | in | I2C clock |
| 52 | 537 | 69 | <![ENDIF]> | SDA | in / out | I2C data |
| 53 | 668 | 69 | <![ENDIF]> | GND | pwr | <![ENDIF]> |
| 54 | 787 | 69 | <![ENDIF]> | VDD | pwr | <![ENDIF]> |
| 55 | 912 | 69 | <![ENDIF]> | din<0> | in | input data |
| 56 | 1038 | 69 | <![ENDIF]> | din<16> | in | " |
| 57 | 1162 | 69 | <![ENDIF]> | din<1> | in | " |
| 58 | 1287 | 69 | <![ENDIF]> | din<17> | in | " |
| 59 | 1412 | 69 | <![ENDIF]> | din<2> | in | " |
| 60 | 1537 | 69 | <![ENDIF]> | din<18> | in | " |
| 61 | 1662 | 69 | <![ENDIF]> | din<3> | in | " |
| 62 | 1787 | 69 | <![ENDIF]> | din<19> | in | " |
| 63 | 1912 | 69 | <![ENDIF]> | din<4> | in | " |
| 64 | 2037 | 69 | <![ENDIF]> | din<20> | in | " |
| 65 | 2162 | 69 | <![ENDIF]> | din<5> | in | " |
| 66 | 2288 | 69 | <![ENDIF]> | din<21> | in | " |
| 67 | 2412 | 69 | <![ENDIF]> | din<6> | in | " |
| 68 | 2537 | 69 | <![ENDIF]> | din<22> | in | " |
| 69 | 2662 | 69 | <![ENDIF]> | din<7> | in | " |
| 70 | 2787 | 69 | <![ENDIF]> | din<23> | in | " |
| 71 | 2912 | 69 | <![ENDIF]> | din<8> | in | " |
| 72 | 3037 | 69 | <![ENDIF]> | din<24> | in | " |
| 73 | 3162 | 69 | <![ENDIF]> | din<9> | in | " |
| 74 | 3288 | 69 | <![ENDIF]> | din<25> | in | " |
| 75 | 3437 | 69 | <![ENDIF]> | din<10> | in | " |
| 76 | 3780 | 412 | <![ENDIF]> | din<26> | in | " |
| 77 | 3780 | 537 | <![ENDIF]> | din<11> | in | " |
| 78 | 3780 | 662 | <![ENDIF]> | din<27> | in | " |
| 79 | 3780 | 787 | <![ENDIF]> | GND | pwr |  |
| 80 | 3780 | 912 | <![ENDIF]> | VDD | pwr | <![ENDIF]> |
| 81 | 3780 | 1037 | <![ENDIF]> | din<12> | in | input data |
| 82 | 3780 | 1162 | <![ENDIF]> | din<28> | in | " |
| 83 | 3780 | 1287 | <![ENDIF]> | din<13> | in | " |
| 84 | 3780 | 1412 | <![ENDIF]> | din<29> | in | " |
| 85 | 3780 | 1537 | <![ENDIF]> | GND | pwr | <![ENDIF]> |
| 86 | 3780 | 1662 | <![ENDIF]> | VDD | pwr | <![ENDIF]> |
| 87 | 3780 | 1787 | <![ENDIF]> | din<14> | in | input data |
| 88 | 3780 | 1912 | <![ENDIF]> | din<30> | in | " |
| 89 | 3780 | 2037 | <![ENDIF]> | din<15> | in | " |
| 90 | 3780 | 2162 | <![ENDIF]> | din<31> | in | " |
| 91 | 3780 | 2287 | <![ENDIF]> | flag<0> | in | flag bit<0> (G-Link mode only) |
| 92 | 3780 | 2412 | <![ENDIF]> | flag<1> | in | flag bit<1> (G-Link mode only) |
| 93 | 3780 | 2537 | <![ENDIF]> | FF | in | forces ff1/ff0 symbols (G-Link mode only) |
| 94 | 3780 | 2662 | <![ENDIF]> | conf_negedge | in | Data is read on falling edge of clk when “1”. On the rising edge if “0” |
| 95 | 3780 | 2787 | <![ENDIF]> | VDDA4 | pwr | PLL power |
| 96 | 3780 | 2912 | <![ENDIF]> | GND | pwr | <![ENDIF]> |
| 97 | 3780 | 3065 | <![ENDIF]> | clkLHCn | in | Differential 40.08 MHz clock input (minus) |
| 98 | 3780 | 3185 | <![ENDIF]> | clkLHCp | in | Differential 40.08 MHz clock input (plus) |
| 99 | 3780 | 3312 | <![ENDIF]> | clkLHC | in | 40.08 MHz input clock |
| 100 | 3780 | 3437 | <![ENDIF]> | selectDiff | in | Selects the 40.08 MHz clock source (pull-up) |

<![ENDIF]> <![ENDIF]> Bond pad 1 <![ENDIF]> <![ENDIF]>

<![ENDIF]> <![ENDIF]> (0,0) “LOGO” <![ENDIF]> <![ENDIF]>

<![ENDIF]> <![ENDIF]> Bond pad 100 <![ENDIF]> <![ENDIF]>

Begin forwarded message:

> From: "Paulo Moreira" <Paulo.Moreira@cern.ch>
> Date: Wed Dec 04, 2002  02:52:42 PM Europe/Zurich
> To: "Alex Kluge" <Alexander.Kluge@cern.ch>
> Subject: ASIC_PINOUT.doc
>
<Attachment missing><Attachment missing><Attachment missing><Attachment missing><Attachment missing><Attachment missing><Attachment missing><Attachment missing><Attachment missing><Attachment missing><Attachment missing><Attachment missing><Attachment missing><Attachment missing><Attachment missing><Attachment missing><Attachment missing>Pin assignments: sorted byPin assignments: sorted bybond pad number
>
> § Bond pads are numbered from 1 to 100. They are numbered 
> counter-clockwise starting at the upper right corner;
>
> § The origin of the coordinates (point (0,0)) is the lower left 
> corner;
>
> § The (X,Y) coordinates are the centre of the bond pads;
>
> § The ASIC dimensions are 3850 mm´3850 mm (Extra 20 mm per side 
> might have to be added to account for the scribe line. In case of need, 
> I could send you a sample of the ASIC.)
>
> § To facilitate identifying the critical signals:
>
> o Ground signals marked green
>
> o Power signals marked red
>
> o Fast serial signals marked blue
>
> § Signals marked blue will require controlled impedance 
> transmission lines:
>
> o Signal ld_cathode: 25 Wtransmission line (both bond pads 7 and 
> 8 connect to the same line)
>
> o Signals serial_line_p and serial_line_p: 50 Wcoplanar 
> transmission line (bond pads 13 and 14 connect to one conductor of the 
> coplanar transmission line and the bond pads 15 and 16 to the other)
>
> § The package should contain a GROUND and a POWER plane.
>
> § All power signals must be directly connected to the power 
> plane. These signals are VDD, VDDA1, VDDA2, VDDA3 and VDDA4.
>
> § The two signals called “ld_anode” must be also directly 
> connected to the power plane.
>
> § At least three ground pins must be made also thermal pins. If 
> possible, these pins should be located under the ASIC area.
>
>